## Slide 1: Y12 Networks L1: Model answers
Y12 Networks L1: Networks: LAN, WAN and hardware
Model answers. Compare them with your notes and add anything you missed in a different colour.

## Slide 2: Task 1A: what is a network?
ANSWERS
A network: two or more computing devices connected, by cable or wireless, so they can transmit data
Advantages (OCR mark schemes): share hardware, files and the internet connection; communicate between machines; any machine can be used; central security, backup and updates; easier to maintain
Disadvantages: malware and viruses spread more easily; if a server fails, connected computers may stop working; heavy traffic can slow computers; data is more widely available so security is more of a risk
Examples: small, a home network or a classroom; large, a school, a company or the internet

## Slide 3: Task 1B: LAN vs WAN
ANSWERS
Feature | LAN | WAN
Geographic scope | Small area: a home, office or building | Large area: cities, countries, continents
Speed | High speed, e.g. 100 Mbps to 10 Gbps | Slower, varies with the technology
Ownership | One person or organisation owns and maintains it | Several telecoms providers and public infrastructure
Examples | Home Wi-Fi, school computer labs, office networks | The Internet, leased lines, public Wi-Fi hotspots
Is the internet a LAN or WAN? | No | Yes: the biggest WAN, a network of networks

## Slide 4: Task 2A: hardware (1/2)
ANSWERS
Device | What it does | LAN or WAN?
Modem | Turns digital data into analogue signals for phone or cable lines, and back, to reach the ISP | WAN
Router | Routes data between networks, such as a LAN and the internet | Both: the edge of the LAN
Switch | Connects LAN devices and sends data only to the device it is for | LAN

## Slide 5: Task 2A: hardware (2/2)
ANSWERS
Device | What it does | LAN or WAN?
Hub | Connects devices in a LAN but copies all data to every device, so traffic floods the network | LAN
WAP | Creates a wireless LAN by connecting to a wired router or switch | LAN
NIC | Lets a computer connect to a network, wired or wireless | Both

## Slide 6: Task 2A: cables
ANSWERS
Cable | Bandwidth, cost and noise | Typical use
Twisted pair | Low bandwidth, cheapest, most affected by noise | Telephone and data networks, office LANs
Coaxial | Moderate bandwidth, costs more than twisted pair but less than fibre, less affected by noise | Aerial and cable TV feeds, linking radio equipment
Fibre optic | Highest bandwidth, most expensive, light so not affected by electrical noise | Long distance links between cities and countries, data centres

## Slide 7: Task 2B: the drawing
ANSWERS
Head office LAN: computers, printer and server cabled to a switch (not a hub), a WAP for Wi-Fi, and a router with a modem at the edge
Branch office LAN: 5 computers on a switch with its own router and modem
The two sites joined across the internet: this part is the WAN, owned by telecoms companies, and each LAN is owned by the company
Cables labelled: twisted pair inside the buildings, fibre optic for a long run or a link between switches, with a reason
Justify: a switch sends data only to the right device so there is less traffic and it is faster, a hub floods every device

## Slide 8: Example: a LAN and WAN diagram
LAN: head office
Router
PC
PC
Printer
Small area, one site. Owned and managed by the company.
LAN: branch office
Router
PC
PC
Printer
Small area, another site. Owned and managed by the company.
WAN: large area, links the LANs over leased lines and the internet, owned by telecoms companies

## Slide 9: Task 3: debate points
ANSWERS
Cables: faster, steadier and not weakened by walls or distance, and fibre optic resists noise best. But every computer needs a cable run and a switch port, so adding or moving one is harder
Wi-Fi: no cable runs, laptops can move, a new computer joins quickly and a WAP is cheap. But the signal weakens through walls and distance, and a WAP's speed is shared
Hardware: cables need a switch, a NIC and a cable type. Wi-Fi needs WAPs and wireless NICs, and each WAP is still cabled to the switch
Best answer: use both. Cable the server, printer and desktops, and use Wi-Fi for laptops and visitors
Push question: link the head office to the branch. The link between the sites is the WAN, run over third party lines owned by telecoms companies

## Slide 10: Example: cables or Wi-Fi in the head office
CABLES
Server
Router
Printer
Switch
PC
PC
PC
PC
PC
PC
PC
PC
PC
PC
Every computer is cabled to the switch with twisted pair. The router links on to the branch.
WI-FI
Server
Router
Printer
Switch
WAP
PC
PC
PC
PC
PC
WAP
PC
PC
PC
PC
PC
Solid line: cable. Dashed line: wireless. The WAPs are cabled to the switch and the computers need wireless NICs.