## Slide 1: 5-A-DAY on SmartRevise
STARTER
Log in and complete today's 5-A-DAY.
5 minutes

## Slide 2: Y12 Networks L3: Build the network: hardware, client-server and peer-to-peer
OCR A Level Computer Science H446, 1.3.3 Networks

## Slide 3: Today's objective
To describe the purpose of common network hardware
To compare client-server with peer-to-peer networks

## Slide 4: Task 1: Retrieval
TASK
Answer three questions on L2 with no notes.
5 min
OneNote: Lesson Tasks, Task 1

## Slide 5: Task 2: Identify the hardware
TASK
Identify each piece of hardware from its photo and explain what it does, then answer the exam question on switches.
10 min
OneNote: Lesson Tasks, Task 2

## Slide 6: Hardware you need to know
Device | Purpose
Modem | Converts digital to analogue and back for a phone or cable line
Router | Connects networks together, forwards data between them
Switch | Active, works at the data link layer: sends data only to the device it is addressed to, using MAC addresses
Hub | Passive, works at the physical layer: broadcasts to every connected device, so it floods the network
WAP | Creates a wireless LAN, connects to a wired router or switch
NIC | Connects a device to a network, holds the MAC address (physical and data link layer)

## Slide 7: Cables
Twisted pair
Cheapest, lowest bandwidth, affected by noise
Coaxial
Moderate bandwidth and cost, less affected by noise
Fibre optic
Highest bandwidth, immune to electrical noise, most expensive

## Slide 8: LAN or WAN?
LAN
Small area, one site, owned by the organisation, connected by UTP, fibre or Wi-Fi
WAN
Large area, links LANs together, infrastructure leased from telecoms companies

## Slide 9: Task 3: Build a LAN
TASK
Build a peer-to-peer LAN, then convert it to client-server.
25 min
OneNote: Lesson Tasks, Task 3

## Slide 10: Client-server or peer-to-peer?
Client-server
Server controls access and security, backups and the shared file store. Easier to manage but costly, needs specialists and the server is a single point of failure.
Peer-to-peer
Every peer is equal and serves its own files. Cheap and easy but each peer looks after its own security and backups.

## Slide 11: Task 4: Design and justify
TASK
Answer the real exam questions on client-server and peer-to-peer.
15 min
OneNote: Lesson Tasks, Task 4

## Slide 12: Task 5: Draw the network
TASK
Use OneNote's drawing tools to draw the network you built.
5 min
OneNote: Lesson Tasks, Task 5

## Slide 13: Plenary
Hub or switch: which and why?
Client-server or P2P: which for a school?
Craig'n'Dave practice: one advantage and one disadvantage of client-server over P2P
Next lesson: the TCP/IP stack

## Slide 14: Check together
ANSWERS

## Slide 15: Task 2: the hardware (Craig'n'Dave 05-1)
ANSWERS
Device | From the Craig'n'Dave answer deck
NIC | Receives and sends electrical signals. Every device connected to a network needs one. Often integrated directly into a motherboard. Assigned a physical MAC address by the manufacturer
Router | Receives packets on a network and forwards them to the correct destination based on the IP address. Is intelligent and uses a table and algorithm to decide the best route onwards
WAP | Allows devices in a network to connect to the network wirelessly. Connection distance varies, around 100 meters
Switch | Connects devices to other devices on a network. Is intelligent and uses packet switching to send data on to specific destinations based on the hardware MAC address
Hub | Cheaper than switches but not as common. Simply broadcasts the signal received to all possible destinations it is connected to
Cables | Copper variants are cheap to use and still very common. Fibre optic is more expensive but the data capacity is much higher

## Slide 16: H446 Nov 2020, Q1 [3]
ANSWERS
Joins computers/devices together on a LAN
Receives packets/data
Recipient's address is given in packet header/it uses the mac address
Send packets/data
Out the correct port /to the specific computer device

## Slide 17: H046 June 2023 [9] (1/4)
ANSWERS
Levels of response: Mark Band 3 (7-9), Mark Band 2 (4-6), Mark Band 1 (1-3), 0 marks. AO1.1 (2), AO1.2 (2), AO2.1 (2), AO3.3 (3)
AO1, P2P: Each computer can act independently; Each computer is responsible for it's own security and login; Each computer will maintain and possibly share its own connected hardware (printer/external storage/internet connection); Each computer will maintain and possibly share its own secondary storage; If a computer is powered down it's shared resources will not be available; There are no resources not shared by a peer machine; Adding a machine is simple; Very little administration is needed

## Slide 18: H046 June 2023 [9] (2/4)
ANSWERS
AO1, Client Server: All network functionality can be provided by servers; A server is a process running on a machine, usually dedicated to providing these services; A server machine is designed to never be powered down; Login/security is handled centrally; Shared storage may be managed by a server; Shared resources (printer/internet connection etc) my be managed by a server; If a server process or machine fails, network functionality, including the ability login is lost; Adding a new machine can mean installing specialist client software and setting up OS policies; IT skills and a lot of time are needed to administer a client server network

## Slide 19: H046 June 2023 [9] (3/4)
ANSWERS
AO2, P2P: As Zak is looking to expand his staff, P2P would offer flexibility in adding staff ad hoc; Zak's company is still small and may struggle to pay for the IT administrator skills needed for a client server
AO2, Client Server: As Zak's firm is an accountancy firm it will have sensitive customer data; Client server would allow stronger centralised security; As Zak is taking on multiple staff, they may wish to work collaboratively, which shared storage would allow; Zak could share a single printer/other hardware with all staff and not worry about an individual computer being switched on

## Slide 20: H046 June 2023 [9] (4/4)
ANSWERS
AO3: Candidates can conclude either method, but to score in the top MB must have a clear line of reasoning to justify their choice.
Guidance
Full level descriptors are on pages 7 and 8 of the mark scheme PDF: pmt-networks-setB-2020-2024-mark-scheme.pdf
Examiner: some candidates discussed topologies, which was not relevant

## Slide 21: H446 Nov 2020, Q1 [2]
ANSWERS
e.g.
only one point of failure
easier to manage users/access
Easier to backup
Easier to keep data secure.
Technicians can more easily remotely install / monitor.
Guidance
Teacher note (not OCR): 'only one point of failure' is printed as an advantage in this mark scheme. Most sources treat a single server as a single point of failure, which is a drawback. Do not teach it as an advantage.

## Slide 22: Discussion: games developer (Craig'n'Dave 06-1)
ANSWERS
Dedicated servers | Peer-to-peer | Listen server (third option)
Server farms in professional data centres. Costly to set up and maintain. Extremely reliable. Low latency. Same latency for all players. High performance | All data is sent as raw streams to all other computers in the game. No specialist infrastructure required. Number of connections and players is limited. Hard to keep synchronised. Difficult to support new players joining | Half-way between dedicated client-server and peer-to-peer. One client acts as a temporary server. No specialist infrastructure required. Dependent on speed of host internet connection. Host advantage requires lag compensation. Host migration if host leaves