## Slide 1: 5-A-DAY on SmartRevise
STARTER
Log in and complete today's 5-A-DAY.
5 minutes

## Slide 2: Y12 Networks L4: The TCP/IP stack and protocol layering
OCR A Level Computer Science H446, 1.3.3 Networks

## Slide 3: Today's objective
To describe the four layers of the TCP/IP stack
To explain what each layer adds to the data

## Slide 4: Task 1: Layers from memory
TASK
Write the four layers in order with one job each. No notes.
5 min
OneNote: Lesson Tasks, Task 1

## Slide 5: Why layers?
Simpler
Break a hard problem into smaller ones
Specialised
Devices and software work at one layer
Compatible
Different vendors' products work together

## Slide 6: The TCP/IP stack
Application
HTTP, FTP, SMTP: what the app wants to say
Transport
TCP: splits into packets, numbers them, adds port numbers
Internet
IP: adds source and destination IP addresses, routers forward
Link
Adds source and destination MAC addresses, sends frames

## Slide 7: One message going down the stack
Link (frame)
Source MAC 00-B0-D0-86-BB-F7, destination MAC (the router) 00-30-B2-45-BB-E9
Internet (packet)
Source IP 192.168.0.2, destination IP 151.101.0.81, TTL 64
Transport
Source port 50000, destination port 80, packet 1 of 3, checksum
Application
HTTP: GET /index.html

## Slide 8: Task 2: The envelope role play
TASK
Watch the role play of a message going down and up the stack, and record what each layer adds.
10 min
OneNote: Lesson Tasks, Task 2

## Slide 9: What a packet carries
Header
Source and destination IP, protocol, packet number, TTL
Payload
The data being sent
Trailer
Checksum or CRC to detect errors

## Slide 10: MAC or IP?
MAC: unique to the network card, used between devices on the same LAN, changes at every hop
IP: identifies the device on the internet, used from end to end, stays the same
Destination MAC is the router's when the target is on another network
Craig'n'Dave 58 analogy: the MAC tells you who someone is, the IP tells you where they are

## Slide 11: Task 3: Capture a real request
TASK
Capture one web request in Wireshark and label every header.
20 min
OneNote: Lesson Tasks, Task 3

## Slide 12: Python: the stack as dictionaries
def application_layer(message):
# TODO 1: return a dictionary with
# "protocol" set to "HTTP" and "data" set to message
pass
Each layer wraps the one above in a dictionary with a header.

## Slide 13: Task 4: Python: build the stack
TASK
Complete layers_starter.py so a message passes down and up the stack.
15 min
OneNote: Lesson Tasks, Task 4

## Slide 14: Task 5: Exam practice
TASK
Answer the four real exam questions, then the discussion question.
10 min
OneNote: Lesson Tasks, Task 5

## Slide 15: Plenary
Four layers, top to bottom, with what each adds
MAC versus IP in two sentences
Craig'n'Dave practice: explain how the TCP/IP stack is a type of protocol, using layering
Next lesson: DNS, routing and switching

## Slide 16: Check together
ANSWERS

## Slide 17: Task 1 and 2: layers
ANSWERS
Layer | Job | Adds
Application | Chooses the protocol, presents the data | HTTP header
Transport | Splits into numbered packets, checks and resends | Port numbers, sequence, checksum
Internet | Addressing and routing | Source and destination IP, TTL
Link | Sends frames between devices on the same network | Source and destination MAC

## Slide 18: H046 June 2022, Q3 [2]
ANSWERS
1 mark for each completed row up to a maximum of 2 marks:
Transport
Network
Guidance
Accept in any order
Accept Internet instead of Network

## Slide 19: H046 June 2022, Q3 [2]
ANSWERS
1 mark per bullet up to a maximum of 2 marks, e.g:
Allows different layers to be worked on independently
Allows layers to be replaced/upgraded without affecting others
Allows for layers from different providers to be used interchangeably
Guidance
Examiner: candidates that gained marks focused on the concept of layers being independent

## Slide 20: H446 June 2023, Q1(d)(iv) [3] (1/2)
ANSWERS
To apply protocols in order / one after the other
To provide independence of layers / Layers can be modified without affecting other layers / Layers are self-contained
Hides details from previous or next layer(s) / is an abstraction
Each layer is well defined / does a specific job
Breaks tasks down into manageable units / Groups similar protocols together
Improved troubleshooting (easier identification of the layer that causes the issue)
Each layer only communicates with adjacent layers/ simplifies interfacing
Hardware/software can be manufactured to fit into one specific layer

## Slide 21: H446 June 2023, Q1(d)(iv) [3] (2/2)
ANSWERS
Allows for standards for individual tasks/layers to be developed / for compatibility

## Slide 22: H046 June 2025, Q9(b) [2]
ANSWERS
1 mark per bullet up to a maximum of 2 marks:
Create a connection between two devices
Agrees the communication settings
Add error correction data
Agrees the size of the packets they will send /receive.
Splits data into packets
Adds a packet number
Adds the total number of packets
Adds the sequence of packets
Adds the port number the packets should use

## Slide 23: Discussion: MAC versus IP (Craig and Dave)
ANSWERS
MAC addresses are used to route frames on a LAN
IP addresses are used to route packets on a WAN
The packet is wrapped in a frame; the MAC changes at each hop, the IP stays the same