## Slide 1: 5-A-DAY on SmartRevise
STARTER
Log in and complete today's 5-A-DAY.
5 minutes

## Slide 2: Y12 Networks L5: DNS, routing, packet switching and circuit switching
OCR A Level Computer Science H446, 1.3.3 Networks

## Slide 3: Today's objective
To explain how DNS finds an IP address
To compare packet switching with circuit switching

## Slide 4: Task 1: Retrieval
TASK
Answer three layer questions with no notes.
5 min
OneNote: Lesson Tasks, Task 1

## Slide 5: Task 1b: Define and test the commands
TASK
Define dns, ping and traceroute, then test each one on bbc.co.uk, screenshot it and annotate it.
10 min
OneNote: Lesson Tasks, Task 1b

## Slide 6: How DNS works
1 Browser
asks the resolver for the IP of www.example.co.uk
2 Root
points to the .uk TLD server
3 TLD
points to the authoritative server
4 Owner
the domain's own server returns the IP address
5 Resolver
returns it to the browser and caches it

## Slide 7: DNS role cards
Browser
I need the IP of www.example.co.uk. I ask my local resolver.
Resolver
I do the work for the browser and ask each server in turn. I keep the answer.
Root
I only know who looks after each TLD. For .uk: ask the .uk server.
TLD (.uk)
I know who looks after example.co.uk: ask that domain's own server.
Owner
I hold the record. www.example.co.uk is 203.0.113.10.

## Slide 8: Task 2: DNS role play
TASK
Act out finding the IP address of a domain name, then run the dns command in the web terminal to compare.
15 min
OneNote: Lesson Tasks, Task 2

## Slide 9: Routing and TTL
A router looks at the destination IP in its routing table and forwards to the next hop
Every router reduces the TTL by one
At zero the packet is dropped, so it cannot loop forever
Traceroute uses TTL: it sends packets with TTL 1, 2, 3 and notes who replies

## Slide 10: Task 3: Traceroute on a map
TASK
Trace the route to a site, then plot it on a world map.
20 min
OneNote: Lesson Tasks, Task 3

## Slide 11: Task 4: A 30 byte email crosses the internet
TASK
Show how a 30 byte email travels from sender to receiver, then answer the exam question on packet switching.
15 min
OneNote: Lesson Tasks, Task 4

## Slide 12: Packet or circuit?
Packet switching
Data split into packets, each takes the least congested route. Efficient, resilient to failure, packets can arrive out of order.
Circuit switching
A dedicated path is reserved for the whole call. Constant quality and order, but bandwidth is wasted in silence.

## Slide 13: Task 5: Packet or circuit?
TASK
Compare packet and circuit switching, then answer the two exam questions.
10 min
OneNote: Lesson Tasks, Task 5

## Slide 14: Plenary
Explain in four steps how a browser finds a server
One advantage of packet switching, one of circuit switching
Next lesson: consolidate and assess

## Slide 15: Check together
ANSWERS

## Slide 16: Task 1: answers
ANSWERS
1. Application, transport, internet, link
2. The internet layer adds IP addresses. Routers use them to forward packets
3. The link layer

## Slide 17: Task 1b: definitions
ANSWERS
DNS (Domain Name System): turns a domain name into the IP address of the server
ping: sends a small message to another computer and times the reply: the round trip time
traceroute (tracert on Windows): lists the routers a packet passes through, one line per hop, with the time for each

## Slide 18: Task 2: the DNS steps
ANSWERS
Step | Who asks | Who answers | Answer
1 | Browser | Local resolver | Asks for the IP, cache miss
2 | Resolver | Root server | Address of the TLD server
3 | Resolver | TLD server | Address of the authoritative server
4 | Resolver | Authoritative server | IP address of the site
5 | Resolver | Browser | IP address, cached for next time

## Slide 19: H046 June 2016, Q2(a) [3]
ANSWERS
(Customers enter) domain name and this is sent to DNS servers.
DNS servers map this domain to an IP address
If the DNS server can't resolve, it passes the request (recursively) to another DNS server.
DNS Server sends the IP address to browser…
… so it can retrieve the website from server on which it is hosted.
(1 per -, Max 3)

## Slide 20: H046 Nov 2020, Q4(b) [4]
ANSWERS
DNS is used to resolve IP corresponding to URL
Request sent to DNS resolver.
Resolver checks its cache and if it doesn't hold the URL, it passes it in to the TLD Name server which checks its cache and returns the answer or passes on to the..
Authoritative Name Server.
The IP address is returned back up to the requesting client.
Or an error if no resolution can be found.
Guidance
Award the mark for checking of cache at any of the stages but limit to one mark for this aspect.

## Slide 21: Task 4: the 30 byte email (Craig'n'Dave 03-1)
ANSWERS
1 The email application passes the message down. 2 TCP splits it into three 10 byte packets, numbers them and adds a checksum to each
3 The destination IP address is looked up through DNS and added to each packet (IP)
4 Packets are routed to the local ISP, then on from node to node: a node that does not know the destination sends the packet to a higher node with a bigger routing table
5 One packet arrives with a checksum error and is requested again until it arrives correctly
6 Packets continue along the best route, arrive at the destination ISP, then the destination computer
7 TCP puts the packets in the correct order, the protocol bits are stripped off and the data goes to the application

## Slide 22: AS H046 1.3.2 (2019), PMT booklet, Q2(a) [5]
ANSWERS
Data is split into equal sized blocks (called packets)
Each packet has a header of information (including destination address and the place of the packet in the complete message)
(Each packet is placed on the network and) each may travel by a different route
(At each node on the network the destination address is read and the) best route is found
Packets need to be reordered at the destination
Guidance
For 'reordered' accept reorganised or similar, but NOT 'reassembled'.

## Slide 23: H046 June 2023 [2]
ANSWERS
In circuit switching dedicated hardware resources are used for each connection
In packet switching hardware is used for multiple different connections.
OR
In circuit switching the data is sent along one route/stream.
In packet switching packets of data may be sent along multiple different routes/packets may not be in order
Guidance
Marks answers in pairs

## Slide 24: H046 June 2023 [2]
ANSWERS
Circuit switching is less secure if data is intercepted
Packet switching, data is more secure if intercepted/not all packets will be intercepted
Computer networks would involve multiple connections happening concurrently
In packet switching hardware is not tied up with each unique connection / can handle multiple connections simultaneously
Computers pass vast amounts of data which may encounter transmission errors
Packet switching means only resending individual packets instead of the whole data stream
Computers may be transmitting business critical data
Packet switching means any network hardware failures can be mitigated by routing around it.

## Slide 25: Packet or circuit (Craig'n'Dave 03-4 and 60)
ANSWERS
Circuit switching | Packet switching
A route is established between two computers. Dedicated link of fixed bandwidth, guaranteed quality, good for real time video. All data follows the same path. A large part of the network is tied up for the transmission. A lot of bandwidth can be wasted. No store and forward | Data is split into equal-sized packets that may take different routes to reach their destination. Packets need to be reordered at the destination. Maximises use of the network. No fixed physical path, no bandwidth reserved, very little wastage, store and forward