## Slide 1: CPU Performance
OCR J277 1.1.2
Systems architecture 4 of 6. Two lessons.

## Slide 2: Lesson 1 objectives
LESSON 1
1
Explain what is meant by CPU performance.
2
Explain how clock speed affects performance.
3
Explain how the number of cores affects performance.

## Slide 3: Think back
RECALL
What happens in one fetch-execute cycle?
One instruction is fetched, decoded and executed
What is cache?
Small, very fast memory close to the CPU holding frequently used data
Why does the cycle repeat?
A program has many instructions; each pass runs one

## Slide 4: Key words
KEY WORDS
Performance
How quickly a CPU can process instructions.
Clock speed
How many fetch-execute cycles the CPU carries out each second.
GHz
Gigahertz. One billion cycles per second.
Number of cores
How many processing units the CPU has. Each can run the cycle.
Cache size
How much cache memory the CPU has.

## Slide 5: Say the full name
EXAM SKILL
Write this | Not enough on its own
Clock speed | clock, speed
Cache size | cache
Number of cores | cores, core
WATCH OUT These three words earn the marks. The short forms earn none.

## Slide 6: Clock speed
CLOCK SPEED
What is it?
The number of fetch-execute cycles the CPU carries out each second.
How is it measured?
In GHz. 3.2 GHz is 3.2 billion cycles per second.
Effect of increasing
More cycles per second, so more instructions are executed per second. The computer runs faster.

## Slide 7: Which is faster, and why?
WORKED
 | Computer A | Computer B
Cores | 1 | 1
Clock speed | 3.2 GHz | 1.2 GHz
TIP Explain why A is usually faster. Use the words cycles and instructions.

## Slide 8: Number of cores
CORES
What is a core?
A processing unit that can carry out the fetch-execute cycle on its own.
Dual and quad
A dual core CPU has 2 cores. A quad core has 4.
Effect of increasing
More instructions can be processed at the same time, so the computer can be faster.
Limit
The program must be split into parts that can run together.

## Slide 9: Activity
ACTIVITY
Activity to be added here.
10 minutes

## Slide 10: Check understanding
CHECK
What does 3 GHz mean?
The CPU carries out 3 billion cycles per second
How can more cores improve performance?
More instructions can be processed at once
Why is a quad core not always 4 times faster?
The program may not be able to use all the cores at once

## Slide 11: Key Terms Review
KEY TERMS
Term | Cue
Performance | how quickly the CPU ...
Clock speed | fetch-execute cycles per ...
GHz | one ... cycles per second
Number of cores | more cores means more ... at once
Write each meaning in your own words in your workbook.

## Slide 12: Cache size and combining factors
LESSON 2
Which CPU is better, and why?

## Slide 13: Lesson 2 objectives
LESSON 2
1
Explain how cache size affects performance.
2
Explain how the three characteristics work in combination.
3
Answer real exam questions comparing CPUs.

## Slide 14: Think back
RECALL
What is clock speed?
The number of fetch-execute cycles the CPU carries out each second
What is a core?
A processing unit that can run the cycle on its own
What are the three words that earn the marks?
Clock speed, cache size, number of cores

## Slide 15: Cache size
CACHE
What is it?
How much cache memory the CPU has, for example 2 MB.
Effect of increasing
More frequently used instructions and data are kept close to the CPU.
Why that is faster
It is faster to transfer to and from cache than to and from RAM.

## Slide 16: The three characteristics
SUMMARY
Characteristic | Increase it and...
Clock speed | More fetch-execute cycles per second, so more instructions per second
Number of cores | More instructions processed at the same time
Cache size | More data kept close, faster to transfer than from RAM

## Slide 17: Combined effects
COMPARE
 | Computer 1 | Computer 2
Clock speed | 1 GHz | 1.4 GHz
Cache size | 2 MB | 2 MB
Number of cores | 4 | 2
TIP Computer 1 is likely to run a 3D flight simulator faster. Why?

## Slide 18: Explaining in the exam
EXAM SKILL
Identify
Pick the right thing from the information. One mark.
Give
A short fact. No reason needed.
Explain
Say what it is, then say why it makes a difference.
TIP Explain = the point, then the reason. 2 marks means 2 points.

## Slide 19: Activity
ACTIVITY
Activity to be added here.
10 minutes

## Slide 20: Exam practice
EXAM
From OCR J277/01 past papers: June 2024 Q6(c); OCR sample paper Q1(a); OCR sample paper Q1(c); OCR J277 question from the PMT 1.1 topic collection, Q5(b)
Give three characteristics of a CPU that can affect its performance. [3]
Clock speed; cache size; number of cores (a bare 'clock' or 'cores' is not enough)
Computer 1: 1 GHz, 4 cores. Computer 2: 1.4 GHz, 2 cores. Identify one reason Computer 1 is faster at 3D flight simulation. [1]
It has more cores
Explain one reason why the cache size affects the performance of the CPU. [2]
Data is transferred to and from cache faster than to and from RAM, so the CPU is more efficient
Computer A: single core, 3.2 GHz. Computer B: single core, 1.2 GHz. Explain why A will usually run faster. [2]
A has a higher clock speed, so it runs more fetch-execute cycles per second, so more instructions are executed per second

## Slide 21: Key Terms Review
KEY TERMS
Term | Cue
Cache size | how much ... the CPU has
Cache | faster to transfer to and from than ...
Combination | more than one ... changed at once
Write each meaning in your own words in your workbook.